## Slide 1: OSI Model

## Slide 2: Objectives
Why we need the OSI model
What each layer is used for
Give examples of how each layer is used

## Slide 3: OSI Model
Open Systems Interconnect or Interconnection – said both ways
Developed in 1980’s
Latest standard defined in 1996
Describes the way computers or networking devices talk to each other

## Slide 4: Why do we need to know this?
You may use it every day
Helps us troubleshoot connection issues
Issues can arise at any layer when there is connectivity involved
As an example think of a website accessing Google

## Slide 5: Layer 7 – Application layer
Responsible for displaying data
Example includes Outlook, Google Chrome, Windows, etc. Anything that displays the final data to you

## Slide 6: Layer 6 – Presentation layer
Data conversion from one form into another – such as HTML or email
Data compression

## Slide 7: Layer 5 - Session
Handles establishment and tear-down of a connection
Manages requests and responses between applications

## Slide 8: Layer 4 - Transport
Very important layer!
Handles acknowledgements and communications between client and server
Responsible for connection and connectionless protocols
End to end connections and reliability of the connection

## Slide 9: Layer 4 Con’t
Connection based protocol - TCP
  Most all communication over the internet is TCP
  Video, Website traffic, etc.
  Needs connections to guarantee information was sent and received on both sides
Connectionless protocol UDP
  Connectionless protocol
  Gaming, logging
  Doesn’t care if it’s received
  Relies on speed

## Slide 10: Layer 3 – Network Layer
Responsible for logical addressing of devices
IPs!
Responsible for routing between physically connected devices
  BGP, OSPF, RIP, EIGRP
Data is transmitted in packets

## Slide 11: Layer 2 - Link
Responsible for the physical link addressing
Responsible for establishment and termination of links
Connects each device physically – think MAC addresses
Data transmitted in frames

## Slide 12: Layer 1 – Physical
Physical signals – electronic, optical, or other medium such as wireless
Responsible for voltage of the device

## Slide 13: Common Issues
Layers 1-3 typically have the issues
Troubleshooting should be done at all layers

## Slide 14: Conclusion
Each layer is important
All layers work together continuously to create communication